|  | Exterior Installations Installation and Verification Record |
| --- | --- |

PLEASE READ CAREFULLY; This is being provided to you as a tool that you may wish to use in providing a safety and risk management program. You are responsible for providing safety and risk management services. We at Chubb are providing this tool to you in support of our underwriting objectives and we hereby disclaim any obligation to oversee or monitor the adherence to required or otherwise reasonable safety and risk control practices. We further disclaim liability for claims or suits relating to the alleged or actual failure to conduct reasonable safety control practices or relating to the use of or failure to use this document. Please note that neither this tool or any of its components contain every possible operation, inspection requirement or other detail that may be relevant to your project or that may be required by federal or state law, or by local building codes, statutes, or other requirements. This tool is intended only as a guideline, and not as a substitute for consultation with your insurance broker, or for engineering, legal or other professional advice.

| Project Identifier: |  | CM/GC: |  |
| --- | --- | --- | --- |
| Owner: |  | Date: |  |

|  | Inspection Criteria | Responsible Party(ies) |  | Inspected by |
| --- | --- | --- | --- | --- |
| Inspection/Test Category | Description | Yes | No | N/A | Installation Contractor | Contracted with | Comments/Notes | Initial | Date |
| Subcontractor Management | Prior to start of operations, verify the following are in place at a minimum for each selected subcontractor: |
|  | Subcontractor pre-qual process that includes at a minimum: review of last 3 yrs. Experience Modification Rate (EMR), OSHA violations, losses, financial status, and safety culture review/assessment. |  |  |  |  |  |  |  |  |
|  | Signed/executed subcontract agreement. |  |  |  |  |  |  |  |  |
|  | Contract includes hold harmless and indemnification agreements in your favor (to the extent allowable by law). |  |  |  |  |  |  |  |  |
|  | Insurance requirements and limits, to include completed operations coverage, meet contract specifications. |  |  |  |  |  |  |  |  |
|  | Includes primary and non-contributory additional insured status for contractor, its officer/employees, owner, and any others required. |  |  |  |  |  |  |  |  |
|  | Verify valid certificates of insurance and endorsements are in place. |  |  |  |  |  |  |  |  |
|  | An appropriately rated insurance carrier. |  |  |  |  |  |  |  |  |
|  | Signed waiver of subrogation for WC/GL is received. |  |  |  |  |  |  |  |  |

|  | Inspection Criteria | Responsible Party(ies) |  | Inspected by |
| --- | --- | --- | --- | --- |
| Inspection/Test Category | Description | Yes | No | N/A | Installation Contractor | Contracted with | Comments/Notes | Initial | Date |
|  | Where required, verify contractor is licensed to work in/for the city and state where project is located. |  |  |  |  |  |  |  |  |
| Approved Shop Drawings and Specifications | Build in strict compliance with approved specifications and shop drawings. |  |  |  |  |  |  |  |  |
|  | Stamped approvals from all applicable parties including building department, structural engineer and/or architect are received and maintained. |  |  |  |  |  |  |  |  |
|  | RFI’s (request for information) are monitored and followed through to verify completion. |  |  |  |  |  |  |  |  |
|  | Continuous monitoring is conducted as plans change throughout course of project. |  |  |  |  |  |  |  |  |
|  | Constructability reviews are completed to identify conflicts, verify adequacy of specifications, and ensure the projects is designed and built for the climate it is located in. |  |  |  |  |  |  |  |  |
|  | Specifications are specific in areas including, but not limited to, attachment points, attachment processes and water removal systems for exterior wall systems. |  |  |  |  |  |  |  |  |
| Cranes | Are either mobile and/or tower cranes to be used to facilitate these operations? |  |  |  |  |  |  |  |  |
|  | If so, has the Chubb “Crane Installation and Verification Record” section been completed? |  |  |  |  |  |  |  |  |
| Equipment / Material Delivery | Assure all equipment & materials necessary for exterior work is visually inspected to verify compliance with final approved specifications and shop drawings and is damage/defect free upon arrival. |  |  |  |  |  |  |  |  |
|  | Field modifications are not conducted unless approved by all parties including the structural engineer and the owner in writing. |  |  |  |  |  |  |  |  |
| Welding Operations | Welding Operations are monitored and at a minimum the following are completed: |
|  | Verify welders are trained and qualified in accordance with local, state, and federal standards and codes. |  |  |  |  |  |  |  |  |
|  | Document & verify welder’s qualifications. |  |  |  |  |  |  |  |  |
|  | Verify a “Hot Work” program is in place that covers fire protection (extinguishers, fire watch), permit and training requirements. |  |  |  |  |  |  |  |  |
|  | At a minimum, all welds are inspected on a continuous, on-going basis for strength, quality, and completeness. |  |  |  |  |  |  |  |  |
| Curtain Wall/Panel/EIFS Consultant | Utilize third party inspection/engineering firm experienced in building envelope design to assist in inspections, design review, installation, etc. |  |  |  |  |  |  |  |  |
|  | Assure coordination/communication between designer, manufacturer, and installer. |  |  |  |  |  |  |  |  |
| Curtain/Panel Wall Design | When considering curtain panel/walls, design considerations include but are not limited to: |
|  | Prevent transmission of loads from build. |  |  |  |  |  |  |  |  |
|  | Assessing material water absorption properties. |  |  |  |  |  |  |  |  |
|  | Protection against water damage. |  |  |  |  |  |  |  |  |
|  | Installation and maintenance requirements. |  |  |  |  |  |  |  |  |
|  | Completeness of architectural drawings. |  |  |  |  |  |  |  |  |
|  | Type and flexibility of caulking. |  |  |  |  |  |  |  |  |
|  | Fabrication requirements. |  |  |  |  |  |  |  |  |
|  | Attachment points. |  |  |  |  |  |  |  |  |
|  | Dimensional changes. |  |  |  |  |  |  |  |  |
|  | Prevention of failures. |  |  |  |  |  |  |  |  |
|  | To assure proper design and installation of curtain wall systems (non-load bearing walls) certifications are obtained from the designer. |  |  |  |  |  |  |  |  |
|  | Designer certifications are filed prior to installation. |  |  |  |  |  |  |  |  |
| Curtain/Panel Wall Materials Manufacturer | Certifications are obtained from manufacturer/materials suppliers to assure proper installation of curtain wall. |  |  |  |  |  |  |  |  |
|  | Materials certifications are delivered with materials when they are delivered to the site. |  |  |  |  |  |  |  |  |
|  | At a minimum, inspections are conducted for each individual component including attachment points and anchor points during installation. |  |  |  |  |  |  |  |  |
|  | Manufacturer verification and sign off is conducted for each phase of installation. |  |  |  |  |  |  |  |  |

|  | Inspection Criteria | Responsible Party(ies) |  | Inspected by |
| --- | --- | --- | --- | --- |
| Inspection/Test Category | Description | Yes | No | N/A | Installation Contractor | Contracted with | Comments/Notes | Initial | Date |
| Certified Curtain Wall Installer | Warranties are obtained from the manufacturer to assure proper installation of curtain wall systems. |  |  |  |  |  |  |  |  |
|  | Use installers that are approved & certified by the manufacturer. |  |  |  |  |  |  |  |  |
|  | Final certification is provided at completion of installation for each component. |  |  |  |  |  |  |  |  |
|  | Inspection of critical areas included but not limited to, attachment/anchor points and process, piece to piece connections, caulking, torque of bolts specific to application, top flashing on top layer of curtain wall, closure/flashing between curtain wall and masonry, imbeds and welds. |  |  |  |  |  |  |  |  |
| Mockup and Testing of Curtain Walls | Testing conducted as required by applicable ASTM and/or AAMA standards. Testing includes but not limited to: |
|  | Static test for water penetration. |  |  |  |  |  |  |  |  |
|  | Dynamic test for water penetration. |  |  |  |  |  |  |  |  |
|  | Structural wind load performance test. |  |  |  |  |  |  |  |  |
|  | Thermal and sound transmission tests. |  |  |  |  |  |  |  |  |
|  | Air infiltration. |  |  |  |  |  |  |  |  |
|  | Review and verify mock-ups are developed and tested by manufacturer or third-party consultant to assess performance of the system against actual predicted extreme weather conditions typical site location to include wind, rain, and temperature. |  |  |  |  |  |  |  |  |
| Material Storage Area's | Verify storage locations are dry and/or protection from the elements. |  |  |  |  |  |  |  |  |
|  | Verify materials are free from damage and dry prior to installation. |  |  |  |  |  |  |  |  |
| Exterior Wall/ Cladding Inspections | Inspections completed to verify conformance with approved drawings and specifications. Items to inspect include but are not limited to: |
|  | Dead load anchors. |  |  |  |  |  |  |  |  |
|  | Wind load anchors. |  |  |  |  |  |  |  |  |
|  | Slab inserts for curtain walls. |  |  |  |  |  |  |  |  |
|  | Heavy wire masonry ties for anchoring brick veneer to the column. |  |  |  |  |  |  |  |  |
|  | Caulking adhesion. |  |  |  |  |  |  |  |  |
|  | Mortar bonds. |  |  |  |  |  |  |  |  |
|  | Wall penetrations. |  |  |  |  |  |  |  |  |
|  | Weep holes. |  |  |  |  |  |  |  |  |
|  | Windows and doors. |  |  |  |  |  |  |  |  |
|  | Caulking and sealants. |  |  |  |  |  |  |  |  |
|  | Flashing and flashing overlap. |  |  |  |  |  |  |  |  |
|  | Communication/coordination is established btwn wall designer and concrete/steel designer and installers. |  |  |  |  |  |  |  |  |
|  | Verify systems installation is within required design tolerances (inspection of anchor points is critical). |  |  |  |  |  |  |  |  |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| Building Material Inspection (Moisture Meter) | Moisture content of building materials is verified (wood, gypsum board, plaster, concrete, brick, roofing, insulation etc.) prior to installation and finishing (verify interior sides after rain). |  |  |  |  |  |  |  |  |
| Caulking/Sealant Inspections | Inspections completed to verify conformance with approved drawings and specifications. Items to inspect include but are not limited to: |
|  | Storage/shelf-life requirements. |  |  |  |  |  |  |  |  |
|  | Type. |  |  |  |  |  |  |  |  |
|  | Flexibility requirements. |  |  |  |  |  |  |  |  |
|  | Proper application. |  |  |  |  |  |  |  |  |
|  | Proper size of bead. |  |  |  |  |  |  |  |  |
|  | Verify surface being applied is clean, dry and within specified temperature range. |  |  |  |  |  |  |  |  |
|  | Assess need for priming/preparing surface for adherence. |  |  |  |  |  |  |  |  |
|  | Assess need for backer rods (excessive depth). |  |  |  |  |  |  |  |  |
|  | Proper depth of caulk. |  |  |  |  |  |  |  |  |
|  | Correct number of surface bonds. |  |  |  |  |  |  |  |  |
|  | Assess requirement for any structural repairs (caulking does not provide mechanical strength). |  |  |  |  |  |  |  |  |
|  | Routinely inspect installation process. |  |  |  |  |  |  |  |  |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| Exterior Wall Water Intrusion Controls | Verify designed system has secondary means of reducing water infiltration. |  |  |  |  |  |  |  |  |
|  | Verify designed system has detail for an internal system allowing drainage or removal of water preventing entrapment. |  |  |  |  |  |  |  |  |
|  | Routinely inspect installation processes. |  |  |  |  |  |  |  |  |

|  | Inspection Criteria | Responsible Party(ies) |  | Inspected by |
| --- | --- | --- | --- | --- |
| Inspection/Test Category | Description | Yes | No | N/A | Installation Contractor | Contracted with | Comments/Notes | Initial | Date |
| Water Testing Completed Units | Water leakage tests are conducted by independent testing agencies after installation and sealants have cured. |  |  |  |  |  |  |  |  |
|  | At a minimum, testing is conducted as required by appropriate AAMA standards. |  |  |  |  |  |  |  |  |
| Exterior Framing Inspections | Inspections completed to verify conformance with approved drawings and specifications. Items to inspect include but are not limited to: |
|  | Proper size, gauge, configuration of materials. |  |  |  |  |  |  |  |  |
|  | Check for plumb/level on openings, substrate, and framing. |  |  |  |  |  |  |  |  |
|  | Approved fasteners. |  |  |  |  |  |  |  |  |
|  | Approved materials. |  |  |  |  |  |  |  |  |
|  | Proper installation. |  |  |  |  |  |  |  |  |
|  | Framing. |  |  |  |  |  |  |  |  |
|  | Substrate. |  |  |  |  |  |  |  |  |
|  | Studs. |  |  |  |  |  |  |  |  |
|  | Tracks. |  |  |  |  |  |  |  |  |
|  | Clips/Brackets. |  |  |  |  |  |  |  |  |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| EIFS Installation | Regular inspections occur during all phases of Exterior Insulation Finishing System (EIFS) construction. Inspections completed to verify conformance with approved drawings and specifications. Items to inspect include but are not limited to: |
|  | Sheathing. |  |  |  |  |  |  |  |  |
|  | Substrate. |  |  |  |  |  |  |  |  |
|  | Inserts. |  |  |  |  |  |  |  |  |
|  | Insulation. |  |  |  |  |  |  |  |  |
|  | Moisture barrier. |  |  |  |  |  |  |  |  |
|  | Foams. |  |  |  |  |  |  |  |  |
|  | Base Coat. |  |  |  |  |  |  |  |  |
|  | Mesh. |  |  |  |  |  |  |  |  |
|  | Finish. |  |  |  |  |  |  |  |  |
|  | Fittings and attachments. |  |  |  |  |  |  |  |  |
|  | Adhesive preparations. |  |  |  |  |  |  |  |  |
|  | Proper application surface sealants. |  |  |  |  |  |  |  |  |
|  | Major wall penetrations (doors, windows, etc.). |  |  |  |  |  |  |  |  |
|  | Minor wall penetrations (phone, TV, A/C coolant lines, hose bibs, etc.). |  |  |  |  |  |  |  |  |
|  | Specific elements of selected EIFS. |  |  |  |  |  |  |  |  |

|  | Inspection Criteria | Responsible Party(ies) |  | Inspected by |
| --- | --- | --- | --- | --- |
| Inspection/Test Category | Description | Yes | No | N/A | Installation Contractor | Contracted with | Comments/Notes | Initial | Date |
| EIFS Installer/Mfr. | The EIFS contractor is listed as an approved applicator by the manufacturer for the specific EIFS being installed. |  |  |  |  |  |  |  |  |
|  | Installer maintains and provides employee training documentation from mfr. or supplier. |  |  |  |  |  |  |  |  |
|  | Verification is obtained from mfr. that project plans & specs contain sufficient info & detail to provide weather tight bldg. envelope. |  |  |  |  |  |  |  |  |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| Stucco/Plaster Inspections | Inspection include but are not limited to, lathing, lath trim, plaster scratch coat, plaster brown coat and plaster finish. |  |  |  |  |  |  |  |  |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| Structure Openings Inspection | Inspections completed to verify conformance with approved drawings and specifications. Items to inspect include but are not limited to: |
|  | Minimization of mechanical stress. |  |  |  |  |  |  |  |  |
|  | Structure placement. |  |  |  |  |  |  |  |  |
|  | Avoidance of wind, rain, water etc. |  |  |  |  |  |  |  |  |
|  | Selection of materials and thresholds. |  |  |  |  |  |  |  |  |
|  | Vertical off-sets between interior/exterior. |  |  |  |  |  |  |  |  |
|  | Need for additional sealants, flashing and barriers? |  |  |  |  |  |  |  |  |
|  | Attachment materials (nailing tabs, etc.). |  |  |  |  |  |  |  |  |
|  | Attachment points. |  |  |  |  |  |  |  |  |
|  | Proper sealing. |  |  |  |  |  |  |  |  |
|  | Caulking. |  |  |  |  |  |  |  |  |
|  | Flashing. |  |  |  |  |  |  |  |  |
| Reinforced Masonry | Prefabricated unit fabrication process is inspected. Inspections completed to verify conformance with approved drawings and specifications. Items to inspect include but are not limited to: |
|  | Placement and bedding of units. |  |  |  |  |  |  |  |  |
|  | Sizes of members. |  |  |  |  |  |  |  |  |
|  | Sizes of column. |  |  |  |  |  |  |  |  |
|  | Thickness of walls. |  |  |  |  |  |  |  |  |
|  | Provisions for curing. |  |  |  |  |  |  |  |  |
|  | Size and position of reinforcement. |  |  |  |  |  |  |  |  |
|  | Protection from freezing. |  |  |  |  |  |  |  |  |
|  | Inspection Criteria | Responsible Party(ies) |  | Inspected by |
| Inspection/Test Category | Description | Yes | No | N/A | Installation Contractor | Contracted with | Comments/Notes | Initial | Date |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| Masonry Unit Inspection | Inspections completed to verify conformance with approved drawings and specifications. Items to inspect include but are not limited to: |
|  | Masonry units clearly identified showing grade and compressive strength as per approved shop drawings and specs? |  |  |  |  |  |  |  |  |
|  | Masonry units are inspected for quality. |  |  |  |  |  |  |  |  |
|  | Water accumulation prevented in cells during masonry wall construction. |  |  |  |  |  |  |  |  |
|  | Wall reinforcement assessment conducted. |  |  |  |  |  |  |  |  |
|  | Temporary wall bracing, as required. |  |  |  |  |  |  |  |  |
|  | Metal anchors and ties. |  |  |  |  |  |  |  |  |
|  | Need and location of weep holes. |  |  |  |  |  |  |  |  |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| Mortar & Grout | Suppliers submit affidavit certifying required ingredients have been included. Certification verified and inspection includes but is not limited to: |
|  | Compressive strength. |  |  |  |  |  |  |  |  |
|  | Proper storage. |  |  |  |  |  |  |  |  |
|  | Clean and potable water. |  |  |  |  |  |  |  |  |
|  | Proper composition. |  |  |  |  |  |  |  |  |
|  | Mixing. |  |  |  |  |  |  |  |  |
|  | Curing. |  |  |  |  |  |  |  |  |
|  | Application. |  |  |  |  |  |  |  |  |
| Water Intrusion, Mold Prevention Program | Regardless of the operation, each project has a water intrusion/mold prevention plan that includes but is not limited to: |
|  | Written plan addressing prevention of water intrusion & mold growth. |  |  |  |  |  |  |  |  |
|  | Plan addresses response procedures for immediate action identifying and removing sources of water intrusion/mold growth. |  |  |  |  |  |  |  |  |
|  | Utilize 3rd party Eng. firms who specialize in building envelopes to perform review of bldg. design for water tightness. |  |  |  |  |  |  |  |  |
|  | Verify MFR’s specs & installation of materials in locations subject to moisture. |  |  |  |  |  |  |  |  |
|  | Verify use of qualified & mfr. certified installers. |  |  |  |  |  |  |  |  |
|  | Consult w/ building envelope Eng., architect & owner regarding design flaws that may allow water intrusion. |  |  |  |  |  |  |  |  |
| Water Intrusion, Mold Prevention Program | Ensure identified flaws are reviewed, redesigned, incorporated into bldg. plans, communicated to installers & proper installation is verified. |  |  |  |  |  |  |  |  |
|  | Construct bldg. in accordance with specs, engineer and architect drawings and instructions. |  |  |  |  |  |  |  |  |
|  | Regular/routine Inspections material, equipment installation operations. |  |  |  |  |  |  |  |  |
|  | Document pre-existing water damage, intrusion, or mold conditions. |  |  |  |  |  |  |  |  |
|  | Documentation includes photos, written reports, logs etc. & maintained in job files. |  |  |  |  |  |  |  |  |
|  | Water/mold removal equipment available (dehumidifiers, heaters). |  |  |  |  |  |  |  |  |
|  | Moisture monitoring in damp, wet locations, or locations where potential for water intrusion exists. |  |  |  |  |  |  |  |  |
|  | Visual observations for moisture indicators such as mold, water lines in drywall, wet spots, discolored ceiling tiles etc... |  |  |  |  |  |  |  |  |
|  | Conduct regular inspections of potential moisture entry points such as windows, doors, roof systems, membranes, flashing, corners, joints, and exterior penetrations. |  |  |  |  |  |  |  |  |
|  | Refer to Chubb Construction Water Intrusion Resource Guide & Mold Prevention Checklist for addition information. |  |  |  |  |  |  |  |  |

|  | Inspection Criteria | Responsible Party(ies) |  | Inspected by |
| --- | --- | --- | --- | --- |
| Inspection/Test Category | Description | Yes | No | N/A | Installation Contractor | Contracted with | Comments/Notes | Initial | Date |
| Manufacturer Information | Verify manufacturer and building information is delivered to the owner in writing. These items include but are not limited to: |
|  | Construction documents such as drawings, specifications, and blueprints. |  |  |  |  |  |  |  |  |
|  | Warranty information. |  |  |  |  |  |  |  |  |
|  | Safety instructions and requirements. |  |  |  |  |  |  |  |  |
|  | Start up and operation instructions and procedures. |  |  |  |  |  |  |  |  |
|  | Maintenance and service instructions. |  |  |  |  |  |  |  |  |
|  | Installation design plans. |  |  |  |  |  |  |  |  |
|  | Training for owners, maintenance staff, etc. |  |  |  |  |  |  |  |  |
|  | Any training products and resources. |  |  |  |  |  |  |  |  |
|  | Location of utilities and structures. |  |  |  |  |  |  |  |  |
|  | Identification/labeling of controls, piping or other. |  |  |  |  |  |  |  |  |
|  | All punch list items, and inspection report deficiencies addressed and corrected to the satisfaction of the inspection agency and/or manufacturer? |  |  |  |  |  |  |  |  |
| ADD |  |  |  |  |  |  |  |  |  |
| ADD |  |  |  |  |  |  |  |  |  |

VERIFICATION STATEMENT I verify that to the best of my knowledge, the inspections and/or tests set out in this installation and verification record were completed by the responsible party shown, that any recommended corrections were made, and that any reports accompanying these inspections/tests were received for review, file and sign off and (if required) PE/RE stamps.

Name (please print in full)

Initials Date

Chubb is the marketing name used to refer to subsidiaries of Chubb Limited providing insurance and related services. For a list of these subsidiaries, please visit our website at www.chubb.com. Insurance provided by ACE American Insurance Company and its U.S. based Chubb underwriting company affiliates.  This document is advisory in nature and is offered for informational purposes only as a resource to be used together with your professional insurance advisors in maintaining a loss prevention program. The information contained in this document is not intended as a substitute for legal, technical, or other professional advice, nor is it intended to supplant any duty to provide a safe workspace, operation, product, or premises. No liabilities or warranties are assumed or provided by the information contained in this document. Chubb, 202 Hall's Mill Road, Whitehouse Station, NJ 08889-1600.